## Slide 1: PREDICTION CACHES FOR SUPERSCALAR PROCESSORS
WITH VICTIM CACHES AND STREAM BUFFERS
By : Chinni Krinshna Kothapalli
Ameya Deswandikar
Manas K.S
Sanjay Sharma

## Slide 2: MOTIVATION
The current cache designs are inefficient.
Most of the cycles wasted in pipeline stalls due to memory access.
Latency of second and third level caches too high.
Increase in latency degrades machine performance by more than 20%.
Need for a better cache design.

## Slide 3: BASE DESIGN IMPLEMENTATION

## Slide 4: Benchmarks

## Slide 5: BASE DESIGN IMPLEMENTATION
Cache Configuration
  L1 Instruction Cache
  2 Kbyte 4 Way Set associative
  L1 Data Cache
  2 Kbyte 4 Way Set associative
  All other parameters are default values.
  Added switches for victim, prediction and stream buffers:
  -cache:il1v il1v:<sets>:<bsize>:<assoc>:<repl_policy>
  -streambuf:size <size>
  -mpred:size <size>

## Slide 6: PREVIOUS WORK
Victim Caches
  Small fully associative cache.
  Victim cache replaces the main cache entry if it is a hit.
  If the entry is not available in victim cache then it goes to the next level cache is accessed.
  Data from higher cache copied to both L1 and Victim.

## Slide 7: VICTIM CACHE

## Slide 8: PERFORMANCE OF VICTIM CACHE
Chart: 
| Compress | GCC | GO | ijpeg | li | m88ksim | Perl | Vortex
Base | 0.8381 | 0.2286 | 0.3552 | 1.2882 | 0.409 | 0.5542 | 0.2032 | 0.2168
Victim=1 | 0.8381 | 0.229 | 0.3559 | 1.2882 | 0.4122 | 0.6359 | 0.2042 | 0.2171
Victim = 2 | 0.8381 | 0.2295 | 0.357 | 1.2882 | 0.4205 | 1.1466 | 0.208 | 0.218
Victim = 64 | 0.8381 | 0.2559 | 0.4834 | 1.5251 | 0.6553 | 1.1113 | 0.3506 | 0.2817

## Slide 9: PERFORMANCE OF VICTIM CACHE 2 LINE
Chart: 
| Compress | GCC | GO | ijpeg | li | m88ksim | Perl | Vortex
Base | 0.8381 | 0.2286 | 0.3552 | 1.2882 | 0.409 | 0.5542 | 0.2032 | 0.2168
Victim=1 | 0.8381 | 0.2296 | 0.3576 | 1.2882 | 0.4221 | 1.1472 | 0.2075 | 0.2181
Victim = 2 | 0.8381 | 0.2306 | 0.3607 | 1.2883 | 0.4277 | 1.1486 | 0.2138 | 0.2199
Victim = 64 | 0.8381 | 0.2814 | 0.6159 | 1.7721 | 0.9151 | 1.1113 | 0.6035 | 0.2817

## Slide 10: STREAM BUFFERS
Stream Buffers
  Array of cache lines dedicated to prefetching.
  Stream buffer is checked on a cache miss.
  Can be implemented as FIFO.
  Request forwarded to next level cache when no match in stream buffers.

## Slide 11: STREAM BUFFERS

## Slide 12: PERFORMANCE OF STREAM BUFFERS
Chart: 
| Compress | GCC | GO | ijpeg | li | Perl | Vortex
Base | 0.8381 | 0.2286 | 0.3552 | 1.2882 | 0.409 | 0.2032 | 0.2168
Stream Buffer=2 | 0.8382 | 0.4001 | 0.6277 | 1.6359 | 0.6537 | 0.3727 | 0.4706
Stream Buffer=4 | 0.8382 | 0.4607 | 0.7293 | 1.7341 | 0.7307 | 0.4163 | 0.5733

## Slide 13: PERFORMANCE OF STREAM BUFFERS
Chart: 
| Compress | GCC | GO | ijpeg | li | Perl | Vortex
Base | 0.8381 | 0.2286 | 0.3552 | 1.2882 | 0.409 | 0.2032 | 0.2168
Stream Buffer=2 | 0.8382 | 0.4001 | 0.6277 | 1.6359 | 0.6537 | 0.3727 | 0.4706
Stream Buffer=4 | 0.8382 | 0.4607 | 0.7293 | 1.7341 | 0.7307 | 0.4163 | 0.5733
Stream Buffer=1 | 0.8381 | 0.3359 | 0.5269 | 1.5387 | 0.567 | 0.3101 | 0.3588
Stream Buffer=8 | 0.8382 | 0.4965 | 0.8048 | 1.7919 | 0.7578 | 0.4349 | 0.6732

## Slide 14: DRAWBACKS OF VICTIM CACHES
Victim caches do not perform better with increasing size.
If there are misses in every line there is no benefit.

## Slide 15: PREDICTION CACHES
Both stream buffers and victim cache just use recent history.
Performance can be improved if cache predicted earlier through miss prediction table.
Maintain a history queue of most recent 10 misses in cache.
Implements a concept called “HOTSPOT”.
The queue monitors the data entry control to victim cache and L1 cache.

## Slide 16: PREDICTION CACHES CONTINUED…
I1
I2
I3
I4
I5
I6
I7
I8
I9
I10
MRU
LRU
MISS PREDICTION HISTORY TABLE

## Slide 17: PREDICTION CACHES CONTINUED…
Most misses caused by a cache line is a Hotspot.
The queue maintains a head and a tail.
Deletion of data from head and entry of new data from tail.

## Slide 18: PREFORMANCE OF PREDICTION CACHES
Chart: 
| Compress | GCC | GO | ijpeg | li | m88ksim
Victim=1 | 0.8381 | 0.229 | 0.3559 | 1.2882 | 0.4122 | 0.6359
Prediction=5 | 0 | 0.30568 | 1.152 | 0.55892 | 0.58224 | 2
Prediction=10 | 0 | 0.26201 | 0.53386 | 0.41143 | 1.213 | 2
Prediction=11

## Slide 19: PREFORMANCE OF PREDICTION CACHES
Chart: 
| Compress | GCC | GO | ijpeg | li | m88ksim
Victim=2 | 0.8381 | 0.2295 | 0.357 | 1.2882 | 0.4205 | 1.1466
Prediction=5 | 0 | 0.087146 | 0.84034 | 0.55892 | -1.4031 | 2
Prediction=10 | 0 | 0.043573 | 0.22409 | 0.41143 | -0.78478 | 2
Prediction=11

## Slide 20: PREFORMANCE OF PREDICTION CACHES
Chart: 
| Compress | GCC | GO | ijpeg | li | m88ksim
Victim=4 | 0.8381 | 0.2305 | 0.3604 | 1.2883 | 0.426 | 1.1486
Prediction=5 | 0 | -0.34707 | -0.11099 | 0.55111 | -2.6761 | 2
Prediction=10 | 0 | -0.39046 | -0.72142 | 0.40363 | -2.0657 | 2
Prediction=11

## Slide 21: PREFORMANCE OF PREDICTION CACHES
Chart: 
| Compress | GCC | GO | ijpeg | li | Pearl | Vortex
stream buffer w/o prediction | 0.8381 | 0.3359 | 0.5269 | 1.5387 | 0.567 | 0.3101 | 0.3588
stream buffer with Prediction | 0 | 0.41679 | 0.64528 | 0.10398 | 2.6102 | 4.6437 | 0.78038

## Slide 22: FUTURE WORK
Stream buffers with low latency access.
Data cache implementation for victim cache and stream buffers.

## Slide 23: REFERENCES
1. P. Jouppi, “Improving direct-mapped cache performance by the addition of a small fully-associative cache and prefetch buffers,” 17th Annual International Symposium on Computer Architecture, pages 364-73, May 1990.
2. S. Palacharla and R.E. Kessler, “Evaluating stream buffers as a secondary cache replacement,” Proc. of the 21st International Symposium on Computer Architecture, pages 24-33, April 1994.
3. V. Phalke and B. Gopinath, “A miss history-based architecture for cache prefetching,” International Workshop IWMM 95 Proceedings, pages 381-98, September 1995.
4. I. Farkas, P. Chow, N. P. Jouppi, and Z. Vranesic, “Memory-system design considerations for dynamically-scheduled processors,” Proc. of the 24th Annual International Symposium on Computer Architecture, pages 133-43, June 1997.

## Slide 24: QUESTIONS